## Slide 1: ParkMaster: An in–vehicle, edge–based video analytics service for detecting open parking spaces in Urban environments
Authors:
Victor Bahl (Microsoft Research),
Giulio Grassi, Giovanni Pau (Pierre and Marie Curie University),
Kyle Jamieson (Princeton University)
Presenter: Arjun Prakash
Published: SEC 2017

## Slide 2: Motivations: the search for a parking spot
6.5 minutes to find a parking spot
  (commercial district of San Francisco)
  More traffic congestion
  More pollution
Solutions available for large parking lot
    [An Algorithm for Parking Lot Occupation Detection, CSIM 2008]
Few solution for on-the-road parking
  [Parknet, MobiSys 2010]
  [Caraoke, Sigcomm 2015]
  [City of San Francisco, Sfpark project]
  Expensive systems on the roads or in cars
Need of a cost-free system for on-the-road parking monitoring

## Slide 3: Key Technologies
Image Processing
    Has made significant Accuracy advancements
    Has provided an array of research topics
Advanced Mobile devices
    High Quality camera
    Are capable of running image-based Machine Learning algorithms
Cloud services
    Are available for implementing latency-critical applications out to the edge

## Slide 4
CLOUD
ParkMaster
3 PARKINGS
AVAILABLE
2 PARKINGS
AVAILABLE
?
3 PARKINGS
AVAILABLE
Notes: Mobile Application on car edge detects location of detected vehicles and upload data to cloud
cloud service maintains real time database

## Slide 5: ParkMaster
Camera of driver’s smartphone as sensor for on-the-road parking availability
Contributions:
  Close to zero-cost system for parking availability monitoring
  Lightweight tracking algorithm
  In-frame car localization algorithm

## Slide 6: ParkMaster: Overview
Parked Car Detection and Counting
Difference between number of parked cars and total number of parking spots
  Lower GPS requirements for accuracy
  Total number of parking spots per road easier to get
In-cloud DB stores estimated parking availability

## Slide 7: Challenges
Resource limitation
Concept to be applied in Real cities
Parking spot should be a legal one
Detailed maps with exact parking space coordinates.

## Slide 8: ParkMaster: Overview

## Slide 9: Empty Space Detection
Edge detection
  Empty space ≠ Parking spot
  An accurate map of each parking spot is needed to localize empty space
EMPTY SPACE
DETECTED!
Empty space detected!
Position: 48.8462, 2.3544
±10 meters
Position: 48.8442, 2.3534
Position: 48.8452, 2.3544
Position: 48.8462, 2.3554
Position: 48.8472, 2.3564

## Slide 10: ParkMaster’s Cascade Classifier
Classifier is based on Viola-Jones
  One-time offline training
    On server
    Extract vehicles main features
  Training output used at run-time to detect cars
    On the phone
  Detection on smartphones: performance
    5.78 fps (Galaxy S4)
    10.44 fps (Galaxy S6)

## Slide 11: Calibration on-the-go
3D
XC , YC , ZC
vC ,
2D
uC
Translation from 2D frame system to 3D real world system
Camera calibration is needed
  Intrinsic camera parameters
    Focal length
  Extrinsic camera parameters
    Camera rotation and translation

## Slide 12: Calibration on-the-go
Classical calibration with well-known patterns
  [An efficient Obstacle Awareness Application for Android Mobile Devices, ICCP 2014]
  Not feasible
    Needed every time the phone is placed on the dashboard
Automatic on-the-go calibration process
  Beginning of a drive, road signs are detected
    Well-know size and elevation from the ground

## Slide 13: Car Localization
3D
2D
Translation from 2D frame system to 3D real world system
  Given the camera parameters, at each point in the frame correspond multiple points in the 3D world.
  We need to fix one of the axis in the 3D system
    Assumptions: cars lay on the ground

## Slide 14: Car counting
On the cloud
  Clustering on coordinates set
    DBSCAN
  Heuristics to decrease the error
    Camera-Vehicle distance
    Cluster size: multiple detections
Cloud’s estimate always corresponds to the most recent drive on that road
Notes: DBSCAN: Density Based Spatial Clustering of Applications with Noise

## Slide 15: Implementation
The edge components
  Android Smartphones
    Samsung Galaxy S4 and S6, LG Nexus 5
  OpenCV 2.4
    Cascade Classifier trained with:
      1,202 positive samples
      719 negative samples
    Available at www.github.com/grassig/parkmaster/
Cloud
  Azure Mobile Service
  MongoDB
  Google Snap Road API

## Slide 16: Evaluation
Notes: We now move to the evaluation of ParkMaster

## Slide 17: Experiments overview
Micro-benchmarks
  Car detection accuracy and performance
  Impact of processing power in car detection accuracy
  Object localization accuracy
Full system
  On-the-road experiments driving in 3 different cities

## Slide 18: Experiments on the road
Place | Distance | Unique distance | Parking spots | Parked cars
EU-village (Sant’Angelo) | 17.9 Km | 3.3 Km | 1,381 | 710 cars
EU-City (Paris) | 38.4 | 7.9 | 3,527 | 2,892
USA-city (Los Angeles) | 41.0 | 19.3 | 3,268 | 2,294
Totals | 97.3 | 30.5 | 8,176 | 5,896

## Slide 19: Village: Sant’Angelo in Vado
Italian village
  No tall buildings
  More space between cars
  Distance driven: 17.9 KM
  Parking spots: 1,381
  Parked cars: 710
Red points: streets with parking space
Blue points: roads with no legal parking

## Slide 20: EU City: Paris
European City
  Tall buildings
  Short space between cars
  Stop and go mobility
  Distance driven: 38.4 KM
  Parking spots: 3,527
  Parked cars: 2,892
Red points: streets with parking space
Blue points: roads with no legal parking

## Slide 21: US City: Los Angeles
US City
  Tall buildings
  Some space between cars
  Stop and go mobility
  Distance driven: 41.0 KM
  Parking spots: 3,268
  Parked cars: 2,294
Red points: streets with parking space
Blue points: roads with no legal parking

## Slide 22: Evaluation Metrics
True positives
False positives

## Slide 23: Evaluation Metrics
Car counting accuracy
ParkMaster: 5 cars
Ground Truth: 4 cars
Missed
23
Notes: Error: parked cars – parked cars counted

## Slide 24: ParkMaster: Overall accuracy
Chart: %
| USA-city | EU-city | EU-village
TPR | 83.435 | 77.6971 | 91.4085
FPR | 17.3469 | 29.8673 | 15.2062
C.C. Accuracy | 89.2023 | 86.2474 | 92.9727
Notes: Park Master shows better performance in rural environment as compared to urban environment. (larger distance, better localization)

## Slide 25: Users’ perspective
Is there at least a parking spot on the road?
  True Positive
  True Negative
ParkMaster: Yes, there is at least a spot available
ParkMaster: No, road is full

## Slide 26: Parking Availability
Chart: %
| USA-city | EU-city | EU-village
TPR | 90.0382 | 87.2229 | 98.6751
TNR | 75.8729 | 74.477 | 89.6286

## Slide 27: Causes of error
Improvements:
  Computing power at the edge
  Classifier
  Phone’s localization
Place | Classifier | Bounding Box | GPS | Localization | False Positive
EU-city (Paris) | 24.3% | 29.2% | 26.3% | 8.0% | 12.2%
EU-village (Sant Angelo) | 29.6 | 29.8 | 14.4 | 7.0 | 19.2
USA-city (Los Angeles) | 24.5 | 27.8 | 25.1 | 17.1 | 5.6

## Slide 28: Data Usage
Edge – Cloud traffic:
  GPS coordinates (Google Snap-to-Road API)
  Parking analytics
    67 bytes per detection
8 hours driving
  6.1 Megabytes
  Cloud-based solution: 4.8 Gigabytes

## Slide 29: Conclusions
Close-to-zero cost system for parking availability
  90% Accuracy in 2 different metropolis and 1 small village
Position-based tracking system that cope with computing limitations of the edge
Vision-based urban environment monitoring at the edge possible with current technology

## Slide 30: Questions?
Thank you for your attention.
Questions?