## Slide 1
Proprietary + Confidential
Aug. 2017
Andy Rosales, Nevena Golubovic, Chandra Krintz & Rich Wolski
Dept. of Computer Science,
UC Santa Barbara
Where’s the bear? – Automatic Wildlife Image Processing Using IoT and Edge Cloud Systems
Presented by: Arjun Prakash
IotDI’17

## Slide 2: What is Edge Cloud Systems
Notes: Method of optimizing cloud computing systems by performing data processing at edge of network.

## Slide 3: Introduction
Evaluating diversity and health of animals.
Automated Animal classification
Avoiding dangerous human/animal encounters & overlap
Monitoring change in land use

## Slide 4: Digital Photography
Alternative to labor-intensive observation & tracking
Cost effective and scalable
Safe
Increasingly autonomous
  Motion triggered
  IoT devices
Reconyx HC500 Hyperfire

## Slide 5: Deployment and Empirical Methodology

## Slide 6
Deployment and Empirical Methodology

## Slide 7: UCSB Sedgwick Reserve
Motion-triggered Wildlife Camera Traps
6000 acres
11 Camera trap locations
Total: 1.12 Million
Images: 714GB
This study: 238K
Images: 93GB

## Slide 8: Image Classification
Enormous number of images (size and count)
Classification and identification once done by humans
  Now automated by data analysis tools
    Tensorflow
    Other similar packages

## Slide 9: Image Classification: Training
machine learning model
deer
coyote
bear
Process: train a model then use it to classify images
Training set (large, manually labeled, ground truth)
Requires lots of compute power and GPUs (thanks public cloud!)

## Slide 10: Challenges With IoT+Cloud for Wildlife Monitoring
Enormous numbers of images (size and count)
Cameras limited storage & processing power
Remote locations of Cameras: Very costly to upload images
Motion triggered cameras activated due to various factors.
Low Bandwidth Network Intermittent connectivity, shared, costly, high latency
Training
Ecologists
Labeling
Public Cloud

## Slide 11: Where's The Bear (WTB)
Multi-tier IoT system
  Perform classification near where the images are produced: Move the code to the data (images) not vice versa
    Via Edge Clouds: robust, self-managing appliances, on-site
    Low latency, high-bandwidth direct connectivity to cameras
    Local image classification
Public Cloud
UCSB Edge Cloud
Limited resources
= can classify but not train!
High Bandwidth, low latency network

## Slide 12: Edge Cloud
Extract images with animals
Scaled down version of AWS public cloud infrastructure: Eucalyptus
Automatic configuration
Transfer empty images to public cloud
Notes: Elastic compute cloud
Simple storage service

## Slide 13
WTB: Train Model In Public Cloud Using "Fake" Images
Transmit a few "empty" images
from edge to public cloud (fast!)
Empty Images
Public Cloud
Why Fake Images?
What are Fake Images?

## Slide 14: WTB: Train Model In Public Cloud Using "Fake" Images
Transmit a few "empty" images
from edge to public cloud (fast!)
Empty Images
+
Google Images
Subtract background (OpenCV)
Random Images
Produce many 1000s
of labeled training images automatically
Public Cloud

## Slide 15: WTB: Train Model In Public Cloud Using "Fake" Images
Transmit (tiny) model back
to edge cloud (fast!)
Empty Images
+
Google Images
Subtract background (OpenCV)
Random Images
Train the model
machine learning model
Public Cloud

## Slide 16: Where's The Bear (WTB)
Multi-tier IoT system
  Move the code to the data (images) not vice versa
    Via Edge Clouds: robust, self-managing appliances, on-site
      Low latency, high-bandwidth direct connectivity to cameras
        Local image classification using model trained in public cloud
Public Cloud
UCSB Edge Cloud
machine learning model
Model training using "fake" images from "empties"

## Slide 17: Camera’s in Details

## Slide 18: Classification by categorizing images:

## Slide 19
Results:

## Slide 20: False Positive versus False Negatives

## Slide 21: 4890 randomly selected images
Results:
1473
images of interest transmitted
vs.
5.3 hrs vs. 1.6 hrs
Researcher time saved!

## Slide 22
Results when WTB compared with the ‘Real model’
What is the ‘Real Model’
Just to measure the accuracy (%) of proposed model

## Slide 23: WTB Conclusions and Future Work
Conclusion
  Public cloud and edge cloud work together to solve problems
  Can save significant researcher time (automatic classification)
Next steps
  Small animals vs empty images, improving accuracy
  Method to reduce the number of False negative images
  Making edge cloud robust to outage and faults

## Slide 24: Thanks!
Collaborators:
UCSB, CalPoly, UCDavis, Fresno State, Powwow Energy,
Sedgwick Reserve,
UC Extension, Private Growers
Support:
Google, Huawei, IBM Research, Microsoft Research, NSF, NIH, California Energy Commission
ckrintz@cs.ucsb.edu
http://www.cs.ucsb.edu/~ckrintz/racelab.html